# RSS ISO14443 Reader

# Serial Protocol

# 1.030.008.001

# Revision 1.02

November 2002

CONFIDENTIAL

# Prepared by

# R&D Technology Solutionz Limited

# for

# Rapid Smartcard Solutionz

# Table of Contents

1.	DOCUMENT REVISION HISTORY	1

1.1	Change Control	1

1.2	Confidentiality and Copyright	1

2.	Introduction	2

2.1	Document Overview	2

2.2	Audience	2

2.3	Circulation List	2

2.4	Attachments	2

2.5	Limitations	2

2.6	Acronyms	2

2.7	Reference Documents	3

3.	Overview	4

3.1	Conventions	4

4.	Serial Protocol	5

4.1	Communications Parameters	5

4.1.1	Serial Parameters	5

4.1.2	Hardware Handshaking	5

4.1.3	DLE Stuffing	5

4.1.4	Timeouts	6

4.2	Message Format	7

4.2.1	STX	7

4.2.2	Token	7

4.2.3	Message Type	7

4.2.4	Data Length	7

4.2.5	ETX	7

4.2.6	Checksum	7

4.3	Serial Acknowledgement	8

4.3.1	Message Acknowledgement	8

4.3.2	Retries	8

5.	Message Types	9

5.1	Status Request	10

5.2	LED Control	11

5.3	Tag Present	12

5.4	Mifare Read MAD	13

5.5	Mifare Update MAD	14

5.6	Mifare Read Sector	15

5.7	Mifare Rewrite Sector	16

5.8	Mifare Write Sector	17

5.9	Mifare Value Transaction	18

5.10	Mifare Load Key	19

5.11	Send APDU	20

5.12	Send Deselect	21

5.13	Information Message	22

5.14	Error Message	23

6.	Transaction Flow	24

Filename= RSSSerialProtocol.doc

# DOCUMENT REVISION HISTORY

| Rev | Description | Date | Author |
| --- | --- | --- | --- |
| 1.00 | Original | 15/10/2002 | B P Simpson |
| 1.01 | Removed tag-type bit-coding table from Tag Present message and changed ‘Mifare card with MAD’ value. Added document revision number to footer. | 18/10/2002 | B P Simpson |
| 1.02 | Added ‘MAD not Present’ error return code to the Mifare Read MAD message. Corrected the Philips demonstration kit write-key in the Mifare Write Sector message. Added note to Mifare Rewrite Sector and Mifare Write Sector messages regarding block 0 of sector 0. Numerous changes to the Mifare Value Transaction message from implementation. Added ‘Command not supported’ to error message error codes. | 22/11/2002 | B P Simpson |

## Change Control

This document is maintained under change control. Any requests for change should go to:

Rapid Smartcard Solutionz Ltd.

P.O. Box 976

Palmerston North

New Zealand

Ph +64 6 952 3720

Fax +64 6 952 3721

Email: rss-support@rds.co.nz

## Confidentiality and Copyright

( Copyright Rapid Smartcard Solutionz Limited 2002. All rights reserved.

This document is the property of Rapid Smartcard Solutionz Limited. It may not be copied, distributed or recorded on any electronic or other medium without the express written permission of Rapid Smartcard Solutionz Limited.

All material contained in this document which is not readily available in the public domain is regarded as confidential to Rapid Smartcard Solutionz Limited and may not be divulged to any third party without the express written permission of Rapid Smartcard Solutionz Limited.

Rapid Smartcard Solutionz extends authorisation to R&D Technology Solutionz to use this document for its intended purpose.

# Introduction

## Document Overview

This document defines a serial protocol and high level command set for communicating with a RSS ISO 14443 compliant reader device connected to a RS-232 compatible serial port.

## Audience

This document is intended for developers and technicians looking to integrate a RSS ISO 14443 compliant reader with a controller.

## Circulation List

All revisions of this document is to be distributed to the following people:

| DISTRIBUTION SHEET |
| --- |
| Document Status | Released |
| Document Distribution Date | 22/11/2002 |
| Name | Organisation | Country |
| Andrew Rushworth | R&D Technology Solutionz | New Zealand |
| Bevan Johnson | R&D Technology Solutionz | New Zealand |
| Braden Simpson | R&D Technology Solutionz | New Zealand |
| Katie Ogle | Rapid Smartcard Solutionz | New Zealand |

## Attachments

There are no attachments to this document.

## Limitations

This document is intended for review, and as such is subject to change. Future revisions of this paper will be distributed via email to those parties identified in section 2.3.

## Acronyms

AC – Application Code [1]

ACK – Acknowledge (ASCII character 0x06)

AID – Application Identifier

APDU – Application Protocol Data Unit

CID – Card Identifier

DLE – Data Length Escape (ASCII character 0x10)

ETX – End of Transmission (ASCII character 0x03)

FCC – Function Cluster Code [1]

LSB – Least Significant Byte

MAD – Mifare Application Directory [1]

MSB – Most Significant Byte

NAK – Negative Acknowledge (ASCII character 0x15)

RF – Radio Frequency

RFID – Radio Frequency Identification

RSS – Rapid Smartcard Solutionz

STX – Start of Transmission (ASCII character 0x02)

## Reference Documents

[1] Mifare Standardization Group [2002]	“Mifare Application Directory Standardization Note” (Revision 2.3)

The following ISO/IEC standards are referenced in this document:

- 14443 Part 2, Part 3, and Part 4 – Contact-less proximity cards

- 7816 Part 4 – Smart Card Standard for Inter-industry Commands for Interchange

# Overview

A number of communications protocols exist for interacting with a RSS ISO 14443 compliant contact-less reader, however they tend to be either too low-level or are biased towards a specific application, such as access control.

The aim of this protocol is to serve as a higher-level abstraction that exposes the generic reader functionality over a standard serial link without the controller device being required to perform a step-by-step interaction with the card.

## Conventions

The flowing conventions are used in this document:

The C programming language notation for hexadecimal values, the identifier ‘0x’ followed by one or more pairs of hexadecimal digits, is used except where otherwise stated e.g. 0x01, 0xFF, 0x01FF

The ASCII letter codes are used for control codes in place of their hexadecimal representation to distinguish them from data values e.g. STX is used in place of 0x02 when it indicates the start of frame.

A zero-length message is often used as a high level response.  This consists of the standard message format with both length bytes set to 0x00 and no data.

This is an asynchronous peer-to-peer protocol and either the controller or the reader can initiate communications.  The communications are full duplex and both devices are required to be able to transmit and receive simultaneously.

# Serial Protocol

The following sections define the serial protocol used between the host and the RSS ISO14443 Reader.

## Communications Parameters

### Serial Parameters

Communication with the RSS ISO14443 Reader is via a RS-232C (EIA-232) serial connection with the following parameters:

| Parameter | Setting |
| --- | --- |
| Baud Rate | 57,600 |
| Bits per Character | 8 |
| Parity | None |
| Stop Bits | 1 |

### Hardware Handshaking

The Request to Send (RTS) and Clear to Send (CTS) serial control lines are used to provide flow control between the receiver and the transmitter.  When a device wishes to send a message it asserts the RTS line and waits for the CTS line to be asserted by the receiver.  Transmission of a message can only begin when the CTS line is asserted and this should be within 100ms of RTS being asserted.  If handshaking is not required then RTS should be connected to CTS on each device.

### DLE Stuffing

To avoid STX, ETX, ACK, and NAK characters (ASCII characters 0x02, 0x03, 0x06, 0x15 respectively) in the body of the message from being interpreted as control codes a DLE character (0x10) is inserted before that character in the data stream.  In order to send a single DLE character two DLE characters must be sent in sequence.

Example of DLE stuffing:

Original message.

| STX | 0x01 | 0xA0 | 0x00 | 0x02 | 0x10 | 0x41 | ETX | 0xF3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

DLE Stuffing.

| STX | 0x01 | 0xA0 | 0x00 | DLE | 0x02 | DLE | 0x10 | 0x41 | ETX | 0xF3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Notes:

- The body of the message is between the STX and ETX and so the checksum does not require a DLE.

- The inserted DLE characters do not change any length variables in the message.

- If the calculated checksum is 0x10 then care must be taken that the STX from the next message is not misinterpreted.

### Timeouts

Two different timeouts are observed over the serial link:

- The time between characters in a message (inter-character timeout).

- The time between sending a message and receiving an acknowledgement (response timeout).

If the inter-character timeout is exceeded then the receiver should send a NAK to the sender.  If the response timeout is exceeded, and the number of retries has not reached the maximum, then the message should be resent.

| Timeout | Time |
| --- | --- |
| Inter-character | 10 ms |
| Response timeout | 300 ms |

## Message Format

A message consists of two framing bytes (STX and ETX), a token, a message type, data length, message data, and a checksum as shown below:

| STX | Token | Message Type | Data Length | Data | ETX | Checksum |
| --- | --- | --- | --- | --- | --- | --- |
| 0x02 | 0x00 – 0xFF | 0x20 – 0xFF | (MSB) | (LSB) | … | 0x03 | 0x00 – 0xFF |

The following sections define each part of the message format.

### STX

This is a single byte start of frame marker represented by ASCII character 0x02.

### Token

For every new message sent the token is incremented by one, with 0xFF rolling over to 0x00.  This allows the receiver to discard any duplicate messages by comparing the token for the message just received with the token from the previous message received.  On reset the token should be set to zero and the previously received token set to 0xFF to avoid any conflict with the first received message.

### Message Type

This is a single byte that identifies the contents of the message.  A response message has the same message type as the request message but has the most significant bit set e.g.

Status Request 0x20 => Status Response 0xA0

The list of valid message types is given in the Message Types section of this document.

### Data Length

The length of the data section in the message is given by a two-byte data length, which gives a maximum number of data-bytes per message of 65535.  The data length does not include the STX, ETX, Token, Message Type, Checksum, or the data length itself and excludes any inserted DLE characters.  The length is sent in big-endian format with the most significant byte (MSB) first followed by the least significant byte (LSB).  For practical purposes the entire message frame, including checksum, must be less than 1024 bytes as this is the maximum buffer size defined in the reader.

### ETX

This is a single byte end of frame marker represented by ASCII character 0x03.

### Checksum

The checksum is exclusive-or (XOR) of all the bytes in the message between the STX and ETX, excluding any DLE characters that have inserted to escape command bytes.  Note that the checksum is not considered part of the body of the message and so does not require a DLE.

Example message with correct checksum

| STX | 0x01 | 0xA0 | 0x00 | 0x02 | 0x10 | 0x41 | ETX | 0xF2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

## Serial Acknowledgement

### Message Acknowledgement

Every serial message received is acknowledged by the receiver with a positive ACK (ASCII character 0x06) or a negative NAK (ASCII character 0x15), depending on the validity of the message.  An ACK indicates that the message was framed correctly, the length was correct, and the checksum was valid for the data received.  A NAK indicates that one or more of the conditions listed below has occurred:

- Another STX was received before an ETX

- An ETX was received before an STX

- An incorrect number of data bytes were received

- A DLE was not followed by a control code or a second DLE

- The message exceeds the available buffer size

- The checksum calculated does not match the checksum that was received

Note:  The message type validity and the contents of the message data are not checked at this level.

### Retries

If a message is responded to with a NAK then the sender will resend the message up to 3 times before discarding it.  A message that fails every retry is most likely to be incorrectly formatted, oversized, and/or the receiver is no longer connected or receiving data.

# Message Types

The table below lists all the possible message types:

| Hex | Decimal | Command |
| --- | --- | --- |
| 0x20 | 32 | Status Request |
| 0x21 | 33 | LED Control |
| (0x22 – 0x2F) | (34 – 47) | Reserved |
| 0x30 | 48 | Tag Present |
| (0x31 – 0x4F) | (49 – 79) | Reserved |
| 0x50 | 80 | Mifare Read MAD |
| 0x51 | 81 | Mifare Update MAD |
| 0x52 | 82 | Mifare Read Sector |
| 0x53 | 83 | Mifare Rewrite Sector |
| 0x54 | 84 | Mifare Write Sector |
| 0x55 | 85 | Mifare Value Transaction |
| 0x56 | 86 | Mifare Load Key |
| (0x57 – 0x5F) | (87 – 95) | Reserved |
| 0x60 | 96 | Send APDU |
| 0x61 | 97 | Send Deselect |
| (0x62 – 0x6F) | (98 – 111) | Reserved |
| 0x70 | 112 | Information Message |
| 0x71 | 113 | Error Message |
| (0x72 – 0x7F) | (114 – 127) | Reserved |
| (0x80 – 0xFF) | (128 – 255) | Response Types |

Each command is described in detail in the following sections.

## Status Request

This message requests the current status of the reader.  This command may be used as a periodic heartbeat to confirm that the reader is connected and functioning correctly.

Originator: Controller

Format:

| Message Type | 0x20 |
| --- | --- |
| Data Length | 1 |
| Data | Field | Size | Value |
|  | Status Request | 1 Byte | 0x00 |

Response:

| Message Type | 0xA0 |
| --- | --- |
| Data Length | 1 |
| Data | Field | Size | Value |
|  | Current Status | 1 Byte | 0x00 – Normal Status, 0xFF – Major Error Status |

## LED Control

This message sets the current state of the LED display on the reader.

Originator: Controller

Format:

| Message Type | 0x21 |
| --- | --- |
| Data Length | 1 |
| Data | Field | Size | Value |
|  | LED Control | 1 Byte | 0x00 – LED Display Reader Control, 0x01 – LED Display Off, 0x02 – LED Display On, 0x03 – LED Display Flash Fast, 0x04 – LED Display Flash Medium, 0x05 – LED Display Flash Slow |

Response:

| Message Type | 0xA1 |
| --- | --- |
| Data Length | 0 |
| Data | Field | Size | Value |

The LED Display Reader Control setting indicates that the reader has control of the LED display.

## Tag Present

This message informs the controller that a tag has been presented at the reader and is in the read zone.

Originator: Reader

Format:

| Message Type | 0x30 |
| --- | --- |
| Data Length | varies |
| Data | Field | Size | Value |
|  | Tag Type | 1 Byte | see table below |
|  | Tag ID | 4 Bytes | 0x00000000 - 0xFFFFFFFF |
|  | Card Identifier | 1 Byte | 0x00 – 0x0F |
|  | Tag Select Data | varies | varies |

Response:

| Message Type | 0xB0 |
| --- | --- |
| Data Length | 0 |
| Data | Field | Size | Value |

Currently accepted tag type values are:

| Value | Meaning |
| --- | --- |
| 0x00 | Type A card with proprietary application protocol |
| 0x01 | Type B card with proprietary application protocol |
| 0x02 | Type A card with ISO 14443 Part 4 application protocol |
| 0x03 | Type B card with ISO 14443 Part 4 application protocol |
| 0x04 | Mifare card |
| 0x05 | Mifare card with MAD |

The tag select data consists of any information returned from the card during the initial negotiation with the reader when the card entered the read zone.

## Mifare Read MAD

This message tells the reader to read the Mifare Application Directory (MAD) from the specified Mifare card in the read zone.

Originator: Controller

Format:

| Message Type | 0x50 |
| --- | --- |
| Data Length | 4 |
| Data | Field | Size | Value |
|  | Tag ID | 4 Bytes | 0x00000000 - 0xFFFFFFFF |

Response:

| Message Type | 0xD0 |
| --- | --- |
| Data Length | 32 |
| Data | Field | Size | Value |
|  | MAD | 32 Bytes | Formatted MAD Data |

or

| Message Type | 0xD0 |
| --- | --- |
| Data Length | 1 |
| Data | Field | Size | Value |
|  | Read Error | 1 Byte | 0x00 – MAD not Present 0xFF – Tag not Present |

The Mifare Standardization Group document Mifare Application Directory Standardization Note [1] contains further documentation on the MAD.

## Mifare Update MAD

This message updates the Mifare Application Directory (MAD) entry for a given data sector.

Originator: Controller

Format:

| Message Type | 0x51 |
| --- | --- |
| Data Length | 0 |
| Data | Field | Size | Value |
|  | Tag ID | 4 Bytes | 0x00000000 - 0xFFFFFFFF |
|  | Write-key Offset | 1 Byte | 0x00 – 0x1F |
|  | Data Sector | 1 Byte | 0x00 – 0x0F |
|  | AID | 2 Bytes | FCC 0x00 – 0xFF, AC 0x00 – 0xFF |

Response:

| Message Type | 0xD1 |
| --- | --- |
| Data Length | 1 |
| Data | Field | Size | Value |
|  | Update Status | 1 Byte | 0x00 – Update Successful, 0xF6 – Authentication Failed, 0xFF – Tag not Present |

The Mifare Standardization Group document Mifare Application Directory Standardization Note [1] contains further documentation on the MAD.

## Mifare Read Sector

This message is used to read data from the specified sector on the Mifare card.

Originator: Controller

Format:

| Message Type | 0x52 |
| --- | --- |
| Data Length | 6 |
| Data | Field | Size | Value |
|  | Tag ID | 4 Bytes | 0x00000000 - 0xFFFFFFFF |
|  | Sector Number | 1 Byte | 0x00 – 0x0F |
|  | Read-key Offset | 1 Byte | 0x00 – 0x1F |

Response:

| Message Type | 0xD2 |
| --- | --- |
| Data Length | 64 |
| Data | Field | Size | Value |
|  | Sector Data | 64 Bytes | Data from the sector |

or

| Message Type | 0xD2 |
| --- | --- |
| Data Length | 1 |
| Data | Field | Size | Value |
|  | Read Error | 1 Byte | 0xF6 – Authentication Failed 0xFF – Tag not Present |

## Mifare Rewrite Sector

This message is used to rewrite data to an existing sector on the Mifare card where the access block for the sector has already been programmed.

Originator: Controller

Format:

| Message Type | 0x53 |
| --- | --- |
| Data Length | 54 |
| Data | Field | Size | Value |
|  | Tag ID | 4 Bytes | 0x00000000 - 0xFFFFFFFF |
|  | Sector Number | 1 Byte | 0x00 – 0x0F |
|  | Write-key Offset | 1 Byte | 0x00 – 0x1F |
|  | Write Data | 48 Bytes | Data to be written |

Response:

| Message Type | 0xD3 |
| --- | --- |
| Data Length | 1 |
| Data | Field | Size | Value |
|  | Write Status | 1 Bytes | 0x00 – Transaction OK, 0xF1 – Write Error, 0xF6 – Authentication Failed, 0xFF – Tag not present |

Note that the first block (block 0) of sector 0 is reserved for card information and is read-only; hence the first 16 bytes of any data sent to be written to sector 0 will be ignored.

## Mifare Write Sector

This message is used to write data to the specified sector on the Mifare card and includes the writing of the access control block.

Originator: Controller

Format:

| Message Type | 0x54 |
| --- | --- |
| Data Length | 70 |
| Data | Field | Size | Value |
|  | Tag ID | 4 Bytes | 0x00000000 - 0xFFFFFFFF |
|  | Sector Number | 1 Byte | 0x00 – 0x0F |
|  | Write-key Offset | 1 Byte | 0x00 – 0x1F |
|  | Write Data | 48 Bytes | Data to be written |
|  | Access Block | 16 Bytes | Access Block data to be written |

Response:

| Message Type | 0xD4 |
| --- | --- |
| Data Length | 1 |
| Data | Field | Size | Value |
|  | Write Status | 1 Bytes | 0x00 – Transaction OK, 0xF1 – Write Error, 0xF6 – Authentication Failed, 0xFF – Tag not present |

If the key given by the write-key offset fails to authenticate with the sector then the reader will attempt to use both the blank tag key (0xFFFFFFFFFFFF) and the Philips demonstration kit write-key (0xB0B1B2B3B4B5) for authentication before failing.

Note that the first block (block 0) of sector 0 is reserved for card information and is read-only; hence the first 16 bytes of any data sent to be written to sector 0 will be ignored.

## Mifare Value Transaction

This message initiates a value increment or decrement transaction, with or without transfer.

Originator: Controller

Format:

| Message Type | 0x55 |
| --- | --- |
| Data Length | 13 |
| Data | Field | Size | Value |
|  | Tag ID | 4 Bytes | 0x00000000 - 0xFFFFFFFF |
|  | Key Offset | 1 Byte | 0x00 – 0x1F |
|  | Value Command | 1 Byte | 0x00 – Decrement, 0x01 – Increment, 0x02 – Restore |
|  | Value Sector | 1 Byte | 0x00 – 0x0F |
|  | Value Block | 1 Byte | 0x00 – 0x02 |
|  | Transfer Block | 1 Byte | 0x00 – 0x02 |
|  | Value | 4 Bytes | 0x00000000 – 0xFFFFFFFF |

Response:

| Message Type | 0xD5 |
| --- | --- |
| Data Length | 1 |
| Data | Field | Size | Value |
|  | Value Status | 1 Byte | 0x00 – Transaction OK, 0x84 – Transaction Failed, 0xF6 – Authentication Failed, 0xFF – Tag not present |

Note that the value should be in little endian format, e.g. the value 0x12345678 should be sent as 0x78563412.

## Mifare Load Key

This message loads a key into a location in the secure key memory on the reader.

Originator: Controller

Format:

| Message Type | 0x56 |
| --- | --- |
| Data Length | 7 |
| Data | Field | Size | Value |
|  | Key Location | 1 Byte | 0x00 – 0x1F |
|  | Key Data | 6 Bytes | 0x000000000000 – 0xFFFFFFFFFFFF |

Response:

| Message Type | 0xD6 |
| --- | --- |
| Data Length | 1 |
| Data | Field | Size | Value |
|  | Load Status | 1 Byte | 0x00 – Key Load Successful, 0x01 – Invalid Key Location, 0x02 – Invalid Key Length |

## Send APDU

This message sends an ISO 7816 Part 4 APDU command to the contact-less card in the read zone.

Originator: Controller

Format:

| Message Type | 0x60 |
| --- | --- |
| Data Length | varies |
| Data | Field | Size | Value |
|  | Card Identifier | 1 Byte | 0x00 – 0x0F |
|  | Node Address | 1 Byte | 0x00 |
|  | Command APDU | 4 Bytes | Header (CLA, INS, P1, P2) |
|  | Command APDU | varies | Body (Lc, Data, Le) |

Response:

| Message Type | 0xE0 |
| --- | --- |
| Data Length | varies |
| Data | Field | Size | Value |
|  | Response APDU | varies | Body (Data) |
|  | Response APDU | varies | Trailer (SW1, SW2) |

See the ISO/IEC 7816 Part 4 standard for information on APDU commands.

## Send Deselect

This message sends an ISO 14443 Part 4 deselect command to a card in the read zone.

Originator: Controller

Format:

| Message Type | 0x61 |
| --- | --- |
| Data Length | 1 |
| Data | Field | Size | Value |
|  | Card Identifier | 1 Byte | 0x00 – 0x0F |

Response:

| Message Type | 0xE1 |
| --- | --- |
| Data Length | 1 |
| Data | Field | Size | Value |
|  | Result | 1 Byte | 0x00 – Success, 0xFF – Tag not present |

Note: The Card Identifier (CID) in this message is not the same as the Tag ID

## Information Message

This message is used for sending informational messages such as version strings, protocol versions, and serial numbers.

Originator: Reader

Format:

| Message Type | 0x70 |
| --- | --- |
| Data Length | varies |
| Data | Field | Size | Value |
|  | Message Text | varies | ASCII Text String |

Response:

None

On a reset the reader will send its version string, serial number, and protocol version in three separate information messages.

## Error Message

This message is sent by the reader to indicate that an error has occurred.  The error is identified by a two-byte code.

Originator: Reader

Format:

| Message Type | 0x71 |
| --- | --- |
| Data Length | 2 |
| Data | Field | Size | Value |
|  | Error Code | 2 Bytes | 0x0000 – 0xFFFF |

Response:

None

The error codes are as follows:

| Code | Description |
| --- | --- |
| 0x0000 | Unknown message type |
| 0x0001 | Invalid message format |
| 0x0002 | Invalid state for command |
| 0x0003 | Command not supported |
| 0x0004 – 0x0FFF | Reserved |
| 0x1000 - 0x1FFF | Internal Processing Errors |
| 0x2000 – 0x3FFF | Minor System Errors |
| 0x4000 – 0x5FFF | Major System Errors |
| 0x5000 – 0xFFFF | Reserved |

# Transaction Flow

The diagram below shows a typical transaction flow: